cONTRIBUTION:	nTCOyyy.doc	 2002 02 12

working Group:	Network Working Group

title:	10 Digit global title translation

Issues Addressed:	This contribution contains the TELUS view of Bell’s NTCO155 contribution on Global Title Translation.

Source:	Telus Communication
Craig Miller

Floor 18F,

10020 – 100 Street			
Edmonton, Alberta

Tel: 780 493-5448

Distribution:	NTWG Interested Parties

REFERENCE:

FILE NAME:

Notice:	This contribution has been prepared by Telus Communication to assist the Network Working Group as basis for discussion. This should not be construed as a binding proposal on Telus Communication. Specifically, Telus Communication reserves the right to request amendments, modifications or to withdraw of this contribution at any time.

PURPOSE

This contribution provides TELUS’ comments and position with respect to the contribution (NTCO155) submitted by Bell Canada on the TT mapping and GTA replacement 10 DGTT looping prevention method.

BACKGROUND

The TISWG and NTWG have discussed the issue of 10D GTT looping prevention in the LNP environment numerous times without reaching a consensus.  These discussions were suspended due to the lack of any imminent need and a desire for a clear direction from the T1S1 standards body.  TELUS acknowledges that the time to discuss this issue appears appropriate.  T1S1 has approved a standard and there appears to be an industry requirement.

TELUS POSITION

The past TI SWG, NP SWG and NT WG discussions identified numerous methods to prevent CCS7 message looping.    TELUS concludes that the recommendation put forth by NTCO155 is the best fit for the TELUS network at this time and considers it an efficient method from a network architecture perspective for the industry.

RECOMMENDATION

TELUS recommends that the use of “TT mapping and GTAI replacement at the 10D GTT node” method for CCS7 loop prevention be adopted as per the recommendations in NTCO 155.